Re: Supplier verification of compliance to material requirements of AAMA/WDMA/CSA 101/I.S.2/A440-17.

Supplier Name:

Material: Weatherstrip

Supplier Address:

This document indicates that materials supplied to 		comply with the material requirements in Clause 6 of AAMA/WDMA/CSA 101/I.S.2/A440-17 applicable to all windows, doors, TDDs, and skylights including glazing, sash, panel, leaf and frame materials as listed below;

11.5 Weatherstrip and/or weatherseal for non-static joints CPM/DL

Weatherstrip and/or weatherseal shall be secured in position, replaceable, and meet the design qualification provisions of the following Standards, as applicable:

- pile weatherstrip and/or weatherseal: AAMA 701;

- weatherstrip and/or weatherseal inserted into or co-extruded onto a frame or sash member: AAMA 702 or ANSI/BHMA A156.22;

- weatherstrip and/or weatherseal of closed cell elastomer: ASTM C509, Option II;

- weatherstrip and/or weatherseal of dense elastomer: ASTM C864, Option II;

- weatherstrip and/or weatherseal of dense thermoplastic elastomer: ASTM E2203;

- weatherstrip and/or weatherseal of pre-formed silicone rubber: ASTM C1115; and

- weatherstrip and/or weatherseal of flexible PVC: ASTM D2287.

If weatherstrip and/or weatherseal, either dual durometer or a thin flexible fin of rigid vinyl, forms an integral part of a frame or sash member, provision shall be made for the installation of a functional replacement weatherstrip and/or weatherseal tested to show equivalence in accordance with AAMA 701/702 or ANSI/BHMA A156.22.

Acknowledgement of compliance:

Signature:_________________________ 			Date_________________

Position:__________________________

References: North American Fenestration Standard / Specification for windows, doors, and skylights. AAMA/WDMA/CSA 101/I.S.2/A440-17